## Slide 1
www.ntu.edu.sg
Visual AI-Enabled Ergonomic Risk Assessment
Presented by Lor Wen Sin
Supervised by Asst Prof Kim Jinwoo
URECA
Undergraduate Research Programme
Background
Workers’ safety is always our main concern in construction site. However, ergonomic risk such as working posture and time are usually not taken into account comprehensively in risk assessment. The concept of cumulative damage is essential when estimating the ergonomic risk, however, current famous ergonomic risk assessments such as REBA and RULA do not take cumulative damage into account.
Secondly, current posture data collections are relying wearables such as IMU, which causes inconvenience and discomfort to the workers. Hence, our research is trying to:
Estimate the risk possibility of getting injured using ergonomic cumulative damage assessment based on the working behaviour of the workers.
REBA/ RULA | Our Method
Assess Risk Score for Each Activity | Assess Risk % for Each Repetition
Indirect Repetition | Dynamic Damage per Repetition
No Knowledge of Fatigue | Able to Estimate Endurance Limit
Only using Risk Score with Range 1 - 7 | Able to Estimate Risk %
Understand the reliability of visual AI-enabled pose estimation technique compared to wearables-based technique such as IMU for ergonomic cumulative damage assessment.