## Slide 1: Proposal

## Slide 2: Research Question
Can we perform ergonomic cumulative assessment using computer vision with deep learning without wearing any equipment to learn the ergonomic characteristics of expert masons?
Justification:
This research direction is meaningful because in the paper written by JuHyeong Ryu, A.M.ASCE1; Bennett Banting2; Eihab Abdel-Rahman3; and Carl T. Haas, F.ASCE4, titled as ‘Ergonomic Characteristics of Expert Masons’, we can tell from the data that the working posture of an expert mason causes the lowest compression force and moments at the respective body parts. However, the expert may not realize that their certain postures are proper postures, therefore they cannot efficiently teach the apprentices. Hence, a scientific analysis can help us to collect proper postures and train the beginners in a more systematic way.

## Slide 3: Background
To develop from paper written by JuHyeong Ryu, A.M.ASCE1; Bennett Banting2; Eihab Abdel-Rahman3; and Carl T. Haas, F.ASCE4, titled as ‘Ergonomic Characteristics of Expert Masons’.
We would like to introduce cumulative damage ergonomic assessment to the same experiment conducted in the paper mentioned previously. Cumulative Damage is an important risk indicator in ergonomics because some posture might not be considered as risky at that moment, but it causes serious musculoskeletal disorder in a long run.
Another thing we would like to introduce is using only computer vision with deep learning to perform the posture estimation without wearing any suit such as IMU. Wearing a suit while working in construction site is less convenient and less comfortable for workers. In addition, to purchase the suit, the budget is higher compared to only using camera for posture estimation.
In the end, we can compare our outcome in terms of cumulative damage to the outcome in the paper mentioned above. We expect our outcome has some similarity to the outcome in the reference paper, but some differences occur due to the consideration of cumulative damage assessment.

## Slide 4: Technical Framework of CD
Motion Capture
Cumulative Damage
Data
Pre-processing
Validation

## Slide 5: Motion Capture
Normal Camera
Microsoft Kinect Azure DK
Ground Truth
Openpose
3D Coordinates
Accuracy
x
y
z
Low Back Flexion
Arm Elevation

## Slide 6: Experiment for Motion Capture
Session 1
First Course
Standard Wall
Reinforced Wall
Constrained Space
Individual 23kg
Colab 23kg
Colab 35.2kg
1
2~6
6~7
8~10
Session 2
2~6
Standard Wall

## Slide 7: Data Pre-processing (Low Back)
x, y, z, ,
Lever Arm
Load’s Weight
Moments + Forces
Revised version
Symbol | Meaning
BW | Body Weight
H | Body Height
HB | Horizontal Location of the object relative to the body
L | Load Weight

## Slide 8: Data Pre-processing (Low Back)
A
A
By
By
https://health.usf.edu/publichealth/tbernard/~/media/D7F7CFCBC5EF43EBB9A23E592BC84411.ashx
https://www.researchgate.net/publication/40785995_A_revised_back_compressive_force_estimation_model_for_ergonomic_evaluation_of_lifting_tasks
,

## Slide 9: Data Pre-processing (Shoulder)
x, y, z, ,
Lever Arm
Load’s Weight
Moments + Forces
***
is total axial stress
is centric axial stress
is axial stress caused by bending moment
+

## Slide 10: Data Pre-processing (Shoulder)
A
A
or

## Slide 11: Cumulative Damage
***
is average axial stress per cycle
is mean ultimate axial stress
S is normalized axial stress wrt
CD = DPC * Number of Repetitions
Low Back
Shoulder

## Slide 12: Validation – 1st Session
Lumbar Compression Force
Cumulative Damage
Observe and Compare
Benchmark

## Slide 13: Validation – 1st Session
Shoulder Moment
(c) Elbow Moment
Cumulative Damage
Observe and Compare
Benchmark
*The author made a mistake, (c) is elbow moment not hip moment

## Slide 14: Validation – 1st Session
(b) Hip Moment
(d) Knee Moment
Cumulative Damage
Observe and Compare
Benchmark
*The author made a mistake, (b) is hip moment not elbow moment

## Slide 15: Validation – 1st Session
All 1st - session activities
Efficiency
Observe and Compare
Benchmark

## Slide 16: Validation – 2nd Session
Lumbar Compression Force
Cumulative Damage
Observe and Compare
Benchmark

## Slide 17: Validation – 2nd Session
Shoulder Moment
(c) Elbow Moment
Cumulative Damage
Observe and Compare
Benchmark

## Slide 18: Validation – 2nd Session
(b) Hip Moment
(d) Knee Moment
Cumulative Damage
Observe and Compare
Benchmark

## Slide 19: Validation – 2nd Session
All 2nd - session activities
Efficiency
Observe and Compare
Benchmark